Semi-Dynamic Session Types for ABS

---
Motivation - Protocols
- Interactions within a distributed system may require a certain order
- Example: Swapping out a web server for maintenance must adhere to this protocol

---
Motivation - Protocols
Manually ensuring compliance with protocol is…
susceptible to human error
Labor-intensive
Impossible for large systems
Formal specification
+ automatic verification / enforcement can help

---
Motivation – Enforcing Scheduling
- Messages sent in the right order must also processed in that order
- Issue if messages can arrive disordered or endpoints may process them in any order
- Static verification can not prevent this
⇒ processing order must be enforced / corrected at runtime

---
Solution: Combine static & dynamic approaches
- We need a specification language
  → Session Types
- We to verify implementations against a protocol
  → Static verification of call orders etc.
- We need to enforce message processing orders at runtime
  → Schedulers

---
Implementation Environment: ABS Language
- ABS is intended for modeling „distributed, object-oriented“ software
- designed to facilitate its verification
- ABS allows defining schedulers

---
Workflow Overview

---
Structure
- Specification Language
- Static Verification
- Dynamic Enforcement
- Evaluation

---
Specification Language: Session Types
Session Type Capabilities
express interaction (calls, retrieving values)
Branchings & loops
ABS cooperative scheduling (suspension, reactivation)
\mbox{}\\ \GSTInteract{\Controller}{f}{\MainServer}{\checkStatus}.\\ \MainServer \{\\ \mbox{}\quad\begin{aligned} &\GSTResolveC{\MainServer}{f}{\Ok}\ldots,\\ &\GSTResolveC{\MainServer}{f}{\NeedsUpdate}\\ &\quad\ldots\\ &\quad\GSTInteract{\Controller}{f'}{\Proxy}{\divert}\\ &\quad\ldots \end{aligned}\\ \}\\ \ldots

---
Specification Sanity Checks
Specification language allows expressing impossible protocols
Releasing control on non-active participants
Fetching results from unresolved futures
…
⇒ Some basic sanity checks are necessary
A \xrightarrow{f} B:m\ldotp A \uparrow f

---
Specification Sanity Checks –
Analysis by Execution
„A calls m on B and fetches result (before B computes it!)“
abstract state
(captures used
futures etc.)
type components used
as instructions of a program
analysis by transition
relation
A \xrightarrow{f} B:m\ldotp A \uparrow f
\begin{align*} \emptyset &\xrsquigarrow{\mathmakebox[1.5cm]{A \xrightarrow{f} B:m}} \{(f: \text{unresolved})\}\\ &\xrsquigarrow{\mathmakebox[1.5cm]{A \uparrow f}} \color{red}\qquad\text{error!} \end{align*}

---
Structure
- Specification Language
- Static Verification
- Dynamic Enforcement
- Evaluation

---
Static Verification – Compositional Approach

---
Static Verification – Compositional Approach
- every method is verified individually against the session type
- a specification of a method‘s behavior is extracted from a global protocol
- Verification of method AST against local type
⇒ Projection
⇒ Type System

---
Projection - Implementation
- Function
- Extracts parts of behavior relevant to the participant
- Using a set of rules and information from abstract state of validity analysis
\project: \SessionType \times \mathbb{S} \times \Participant \rightarrow \LocalSessionType

---
Projection: Extraction of a localized specification
Global Session Type
\begin{aligned} &\GSTInit{f_0}{A}{\mathit{init}}. \GSTInteract{A}{f_1}{B}{m_1}.\\ &\mbox{}\quad\GSTInteract{B}{f_c}{C}{m_c}. \GSTResolve{C}{f_c}. \GSTFetch{B}{f_c}. \GSTResolve{B}{f_1}.\\ &\GSTInteract{A}{f_2}{B}{m_2}.\\ &\mbox{}\quad\GSTInteract{B}{}{D}{m_d}. \ldots \end{aligned}

---
Projection: Extraction of a localized specification
Global Session Type
Projection on
object B
Object Local Type for B
\begin{aligned} &\LSTReceive{A}{f_1}{m_1}.\\ &\mbox{}\quad\LSTSend{C}{f_c}{m_c}. \LSTGet{f_c}. \LSTPut{f_1}.\\ &\LSTReceive{A}{f_2}{m_2}.\\ &\mbox{}\quad\LSTSend{D}{}{m_d}. \ldots \end{aligned}
\begin{aligned} &\GSTInit{f_0}{A}{\mathit{init}}. \colorbox{bluebg}{$\GSTInteract{A}{f_1}{B}{m_1}$}.\\ &\mbox{}\quad\colorbox{bluebg}{$\GSTInteract{B}{f_c}{C}{m_c}$}. \GSTResolve{C}{f_c}. \colorbox{bluebg}{$\GSTFetch{B}{f_c}. \GSTResolve{B}{f_1}.$}\\ &\colorbox{bluebg}{$\GSTInteract{A}{f_2}{B}{m_2}.$}\\ &\mbox{}\quad\colorbox{bluebg}{$\GSTInteract{B}{}{D}{m_d}$}. \ldots \end{aligned}

---
Projection: Extraction of a localized specification
Global Session Type
Projection on
object B
Object Local Type for B
Projection on
method B::m1
for future f1
Method Local Type for B::m1
\MLSTSend{C}{f_c}{m_c}. \MLSTGet{f_c}. \MLSTPut{f_1}
\begin{aligned} &\GSTInit{f_0}{A}{\mathit{init}}. \colorbox{bluebg}{$\GSTInteract{A}{f_1}{B}{m_1}$}.\\ &\mbox{}\quad\colorbox{bluebg}{$\GSTInteract{B}{f_c}{C}{m_c}$}. \GSTResolve{C}{f_c}. \colorbox{bluebg}{$\GSTFetch{B}{f_c}. \GSTResolve{B}{f_1}.$}\\ &\colorbox{bluebg}{$\GSTInteract{A}{f_2}{B}{m_2}.$}\\ &\mbox{}\quad\colorbox{bluebg}{$\GSTInteract{B}{}{D}{m_d}$}. \ldots \end{aligned}
\begin{aligned} &\colorbox{bluebg}{$\LSTReceive{A}{f_1}{m_1}.$}\\ &\mbox{}\quad\colorbox{bluebg}{$\LSTSend{C}{f_c}{m_c}. \LSTGet{f_c}. \LSTPut{f_1}$}.\\ &\LSTReceive{A}{f_2}{m_2}.\\ &\mbox{}\quad\LSTSend{D}{}{m_d}. \ldots \end{aligned}

---
Verification using a Type System
. . .
Now, method bodies can be verified against local type using a type system
- Specified actions must each be implemented by a corresponding statement
- Control structures must match type branchings / loops
- Correct usage of variables, futures etc. is checked
- Data type checking is left to the ABS compiler
- ...
\MLSTSend{C}{f_c}{m_c}.
\MLSTPut{f_1}
\MLSTGet{f_c}.

---
Verification using a Type System
. . .
Design Goals
- Soundness
- Support current implementation of ABS
- Usability: Leave developers as much freedom as possible
  i. e. allow all additional code that does not influence session
\MLSTSend{C}{f_c}{m_c}.
\MLSTPut{f_1}
\MLSTGet{f_c}.

---
Demo

---
Structure
- Specification Language
- Static Verification
- Dynamic Enforcement
- Evaluation

---
Dynamic enforcement of protocols
What does it take to enforce a protocol?
How far we have progressed in the protocol
Which method activations are allowed next
For every participant
At every point of execution, we need to know…

---
From Specification to Scheduler

---
Session Automata – Example
„Receive call on m as future f, then suspend, then reactivate f“
automaton allows reactivation only, if future to be reactivated belongs to original invocation
Automaton state contains registers for storing futures
p?_f:m.Await(f, f').React(f)
⇒

---
From Specification to Scheduler

---
Scheduling Functions
- Input
  - possible (re-)activations
  - automaton state
- Ouput
  - selected (re-)activation
  - Or nothing → pauses
- Called upon
  - invocations, reactivations, ...

---
Demo

---
Runtime Verification of Method Side Effects
- Specification so far describes only structure of interactions
- but not side-effects of method calls etc.
- Session types are extended with post-conditions for interactions, e. g.
p \xrightarrow{f} q:m\ldotp q \downarrow f \left\langle q.\text{attrib} = 42 \right\rangle\ldots

---
Runtime Verification of Method Side Effects
- Hard to verify statically
- Easy to check at runtime
  - especially since AST is being modified anyway
- By introducing assertions :
⇒
Unit m() {
   …
   if (automatonState == 2)
     assert(attrib == 42);
}
p \xrightarrow{f} q:m\ldotp q \downarrow f \left\langle q.\text{attrib} = 42 \right\rangle\ldots

---
Structure
- Specification Language
- Static Verification
- Dynamic Enforcement
- Evaluation

---
Evaluation – Main Questions
Static Verification
Does the type system meet design goals?
Soundness?
Modeling freedom / Usability?
Dynamic Enforcement
Is method activation order reliably ensured?
How do schedulers affect execution
performance?

---
Evaluation – Type System
Soundness
It has been informally argued that our type validation, projection
and type system rules...
...take the same precautions to ensure soundness as the
theoretical work the SDS-tool is based on
...also ensures soundness where we diverge from the original
work
Tests and examples support this claim
Formal proof remains (time constraints)

---
Evaluation – Type System
Usability – Some Examples
Pro
Contra
Actions not influencing
session always permitted
Even calls
→Half-open systems
Futures can not be communicated
between objects
Session actors must be
instantiated in main block
Session actors are bound to classes
Futures must be stored in fields

---
Evaluation – Dynamic Enforcement
Minimal Scenario: Consecutive Calls
\begin{aligned} &\GSTInit{f}{P}{\mZero}.\\ &(\\ &\quad\GSTInteract{P}{\fmOne}{Q}{\mOne}. \GSTResolve{Q}{\fmOne}.\\ &\quad\GSTInteract{P}{\fmTwo}{Q}{\mTwo}. \GSTResolve{Q}{\fmTwo}\\ &)^*.\\ &\GSTResolve{P}{f} \end{aligned}

---
Evaluation – Dynamic Enforcement
Is invocation order enforced?
Measure: Levenshtein distance between observed invocation
order and intended, alternating order
Model without schedulers increasingly violates order with
higher number of calls
Model with schedulers never violated the order

---
Evaluation – Dynamic Enforcement
Is invocation order enforced?
Measure: Levenshtein distance between observed invocation
order and intended, alternating order
Model without schedulers increasingly violates order with
higher number of calls
Model with schedulers never violated the order

---
Evaluation – Dynamic Enforcement
How is model execution time affected? (user mode)
Constant, slight overhead until certain number of calls (200)
Fast growing overhead at 600+ calls
Multiples of original execution time

---
Evaluation – Dynamic Enforcement
How is model execution time affected? (user mode)
Constant, slight overhead until certain number of calls (200)
Fast growing overhead at 600+ calls
Multiples of original execution time

---
Evaluation – Dynamic Enforcement
Similar observations are made for maximum memory resident set size, though overhead is not as severe

---
Evaluation – Dynamic Enforcement
How do schedulers compare to manual synchronization?
we insert await-statements between the calls
Now, reduced execution time overhead for plain and enforcment models
(schedulers do not have to reorder)
Counterintuitive, since both, caller and callee are being stalled
[Speaker Notes: Should I give percentages of reduction?]

---
Evaluation – Dynamic Enforcement
Manual synchronization takes less time than schedulers
without „await“
with „await“
[Speaker Notes: Should I talk about the experiment, which introduced delays?]

---
Conclusion
- A tool has been developed which...
  - allows to statically verify an ABS model against a session type specification
  - extends models to dynamically enforce behavior which can not be statically guaranteed
- The evaluation showed…
  - the tool can be applied to develop small models in the current ABS implementation
  - order is reliably enforced at runtime
  - at the cost of severe execution time overhead at a high number of calls
    - can be mitigated by manual synchronization

---
Future Work
Lifting modeling restrictions
Allow to store futures in non-fields, share futures between objects, …
Will require more sophisticated analyses
points-to analyses to identify references etc.
Improving liveness properties
Introduce deadlock checks
Improvements on session automata (data-determinism)
...

---
Future Work
Expand condition checking
Use KeY-ABS to try proving conditions statically first
Use runtime verification only when necessary
Comprehensive Case Study
Apply session types to an extensive ABS model
How do usability issues affect the modeling process?
How do schedulers impact performance of complex models?

---
Thank you for listening
projection
global
session automata
...
protocols
dynamic enforcement
local
schedulers
Semi-Dynamic Session Types for ABS
specification validation
static verification
type system
based on
„Session-based compositional analysis for actor-based languages using futures."
„Stateful Behavioral Types for ABS“
by Kamburjan, E., Din, C. C., Chen, T.

---
Image sources
- Google Material Design Icons have been used in this presentation
- Source: https://github.com/google/material-design-icons
- License: Apache 2.0